## Slide 1: Hillsborough County Metropolitan Planning Commission (MPO) Walk/Bike Safety Action Plan
Task 1: Findings of Crash Data and Field Review
Hillsborough County MPO
Prepared for:
Prepared by:
Hillsborough County Bicycle/Pedestrian Advisory Committee (BPAC)
January 11, 2012
URS Corporation

## Slide 2: Agenda
Purpose
Study Areas and Corridors
General Observations
Priority Ranking
Next Steps

## Slide 3: Purpose
The need for a balanced, multi-modal transportation with strategic “enhancements” to provide safer, more convenient and comfortable travel for all users including bicyclists, pedestrians, transit patrons, children, seniors and persons with disabilities.

## Slide 4: Study Areas and Corridors
USF Area
  56th Street - Fowler Avenue to Fletcher Avenue
  42nd Street - Fletcher Avenue to Bruce. B. Downs Boulevard
  46th Street/Skipper Road – Fletcher Avenue to Bruce B. Downs Boulevard
  Bruce B. Downs Boulevard – Fletcher Avenue to City Limits
Carrollwood Area
  Fletcher Avenue – North Boulevard to Nebraska Avenue
  Northdale Boulevard – Dale Mabry Highway to Lakeshore Road
  Bearss Avenue – Dale Mabry Highway to 22nd Street
Town N’ Country / Egypt Lake Area
  Waters Avenue – Sheldon Road to Florida Avenue
  Sligh Avenue / Pinecrest Manor – Benjamin Road to Dale Mabry Highway
  Lambright Road / Sligh Avenue – Dale Mabry Highway to Armenia Avenue
  Hanley Road – Hillsborough Avenue to Waters Avenue
  Sheldon Road – Hillsborough Avenue to Linebaugh Avenue

## Slide 5: Study Areas and Corridors (Continued)
Palm River Area
  78th Street – Madison Avenue to Lee Roy Selmon Expressway
  Maydell Drive – Causeway Boulevard to Adamo Drive
Citrus Park Area
  Gunn Highway – Ehrilich Road to Citrus Park Drive
  Gunn Highway – Citrus Park Drive to Henderson Road
  Gunn Highway – Tarpon Springs Road to Van Dyke Road
Brandon Area
  Parsons Avenue – SR 60 to Martin Luther King Jr. Boulevard
  Mango Road (CR 579) - Martin Luther King Jr. Boulevard to N. of I-4
  Providence Road – Bloomingdale Avenue to SR 60
  Bloomingdale Avenue – US 301 to Lithia Pinecrest Road

## Slide 6
USF
Citrus
Citrus
Carrollwood
NTS
Northwest Hillsborough County
Study Corridor

## Slide 7
Town N’ Country
NTS
West Central Hillsborough County
Study Corridor

## Slide 8
Palm
River
Brandon
NTS
Southeast Hillsborough County
Study Corridor

## Slide 9: General Observations
Intersection Approach Crosswalks
  Unless proven otherwise, include crosswalks at all intersection approaches
  Place crosswalks as close to the intersection as possible
  Parallel to adjacent street
  Ladder crosswalks

## Slide 10: General Observations (continued)
Pedestrian Lighting
  Important to maximize pedestrian visibility
Bike Lane Markings
  Inconsistent bike lane markings are confusing for both motorists and pedestrians; should be consistent with MUTCD
Bike Parking at Bus Stops
  Observed bikes locked to signs, etc.
Debris and Vegetation
  Bike lanes and roadways should be kept clear of debris

## Slide 11: Lighting
Generally insufficient
  Roadway lighting does not necessarily equate to a well lit roadway for pedestrians
  Vehicle lighting versus Pedestrian lighting
  Areas of dark and light
  FDOT Painted Pavement Markings (PPM) and Lighting Standards

## Slide 12: Substandard Lighting

## Slide 13: Standard Lighting

## Slide 14: Lane Striping
As related to Night Time Visibility
  Research supports improving roadway striping to reduce all crashes
  Hypothesis: enhanced striping allows motorists to devote more attention to what is happening in the environment and less to maintaining lane position

## Slide 15: Corridor Priority Ranking
Facility | From | To | 2010 | Crash Data 2006-2011 |  |  |  | Priority Ranking |  | 
 |  |  |  | No. of Crashes | Crashes Per Mile Ratio | Crashes Per 10,000 AADT | Lighting (Dark, Dark-Lighted, Dark-Not Lighted, Dusk) | Composite Factor | Within Area Ranking | Overall Ranking
USF Area |  |  |  |  |  |  |  |  |  | 
56th St | Fowler Ave | Fletcher Ave | 28,100 | 14 | 13.73 | 4.98 | 43% | 11.54 | 3 | 9
42nd St | Fletcher Ave | Bruce B. Downs | N/A | 13 | 14.61 | N/A | 62% | 14.61 | 2 | 6
46th St/Skipper Rd | Fletcher Ave | Bruce B. Downs | 15,100 | 6 | 5.13 | 3.97 | 33% | 4.84 | 4 | 20
Bruce B. Downs Blvd | Fletcher Ave | City Limit | 60,600 | 41 | 22.40 | 6.77 | 34% | 18.49 | 1 | 4
Carrollwood Area |  |  |  |  |  |  |  |  |  | 
Fletcher Ave | North Boulevard | Nebraska Ave | 39,200 | 31 | 31.00 | 7.91 | 32% | 25.23 | 1 | 1
Northdale Blvd | Dale Mabry Hwy | Dawnview Dr | 7,700 | 8 | 11.11 | 10.39 | 50% | 10.93 | 3 | 11
 | Dawnview Dr | Claywell Elementary | 7,700 | 2 | 2.63 | 2.60 | 0% | 2.62 | 4 | 26
 | Claywell Elementary | Lakeshore Rd | 7,700 | 0 | 0.00 | 0.00 | 0% | 0.00 | 5 | 28
Bearss Ave | Dale Mabry Hwy | 22nd St | 51,000 | 59 | 12.69 | 11.57 | 31% | 12.41 | 2 | 8
Town N' Country / Egypt Lake |  |  |  |  |  |  |  |  |  | 
Waters Ave | Sheldon Rd | Anderson Rd | 34,100 | 62 | 22.38 | 18.18 | 2% | 21.33 | 1 | 2
 | Anderson Rd | Dale Mabry Hwy | 45,900 | 31 | 15.58 | 6.75 | 48% | 13.37 | 4 | 7
 | Dale Mabry Hwy | Florida Ave | 33,000 | 58 | 20.86 | 17.58 | 40% | 20.04 | 2 | 3
Sligh Ave/Pinecrest Manor | Benjamin Rd | Dale Mabry Hwy | 14,300 | 9 | 3.88 | 6.29 | 22% | 4.48 | 7 | 22
Lambright Rd/Sligh Ave | Dale Mabry Hwy | Armenia Ave | 25,900 | 8 | 5.93 | 3.09 | 25% | 5.22 | 6 | 19
Hanley | Hillsborough Ave | Waters Ave | 30,500 | 39 | 19.31 | 12.79 | 36% | 17.68 | 3 | 5
Sheldon Rd | Hillsborough Ave | Linebaugh Ave | 47,100 | 36 | 10.84 | 7.64 | 36% | 10.04 | 5 | 12

## Slide 16: Corridor Priority Ranking
Facility | From | To | 2010 | Crash Data 2006-2011 |  |  |  | Priority Ranking |  | 
 |  |  |  | No. of Crashes | Crashes Per Mile Ratio | Crashes Per 10,000 AADT | Lighting (Dark, Dark-Lighted, Dark-Not Lighted, Dusk) | Composite Factor | Within Area Ranking | Overall Ranking
Palm River - Coordination with South Coast Greenway |  |  |  |  |  |  |  |  |  | 
78th St | Madison Ave | Causeway Blvd | 11,000 | 5 | 3.09 | 4.55 | 40% | 3.45 | 3 | 25
 | Causeway Blvd | Lee Roy Selmon | 25,100 | 16 | 8.56 | 6.37 | 38% | 8.01 | 1 | 14
Maydell Dr | Causeway Blvd | Adamo Dr | 2,800 | 3 | 1.48 | 10.71 | 33% | 3.79 | 2 | 24
Citrus Park - Coordination with Upper Tampa Bay Trail |  |  |  |  |  |  |  |  |  | 
Gunn Hwy | Ehrlich Rd | Citrus Park Dr | 12,500 | 5 | 5.81 | 4.00 | 40% | 5.36 | 2 | 17
 | Citrus Park Dr | Henderson Rd | 34,300 | 9 | 7.03 | 2.62 | 11% | 5.93 | 1 | 16
 | Tarpon Springs | Van Dyke Rd | 19,000 | 2 | 1.36 | 1.05 | 100% | 1.28 | 3 | 27
Brandon Area |  |  |  |  |  |  |  |  |  | 
Parsons Ave | SR 60 | M L King Blvd | 28,200 | 23 | 7.62 | 8.16 | 17% | 7.75 | 3 | 15
Mango Rd (CR579) | M L King Blvd | N of I-4 | 13,500 | 15 | 8.15 | 11.11 | 40% | 8.89 | 2 | 13
Providence Rd | Bloomingdale Ave | SR 60 | 18,100 | 30 | 9.29 | 16.57 | 43% | 11.11 | 1 | 10
Bloomingdale Ave | US Hwy 301 | Bell Shoals Rd | 56,400 | 21 | 5.00 | 3.72 | 29% | 4.68 | 5 | 21
 | Bell Shoals Rd | Cade Ln | 28,200 | 4 | 5.13 | 1.42 | 0% | 4.20 | 6 | 23
 | Cade Ln | Lithia Pinecrest | 28,200 | 5 | 6.41 | 1.77 | 0% | 5.25 | 4 | 18

## Slide 17: Corridor Preliminary Recommendations
Facility | From | To | Preliminary Recommendations |  |  |  |  |  | 
 |  |  | Sharrows | Bike Lane | Sidewalks | Midblock Safety (Ped/Rdwy Audit) | Lighting | Roadway/ Intersection Restriping/ Improvement | Transit
USF Area |  |  |  |  |  |  |  |  | 
56th St | Fowler Ave | Fletcher Ave |  |  | P | P | P |  | 
42nd St | Fletcher Ave | Bruce B. Downs | P |  | P | P | P |  | 
46th St/Skipper Rd | Fletcher Ave | Bruce B. Downs |  |  | P |  | P | P | 
Bruce B. Downs Blvd | Fletcher Ave | City Limit |  |  |  |  | P | P | P
Carrollwood Area |  |  |  |  |  |  |  |  | 
Fletcher Ave | North Boulevard | Nebraska Ave |  | P |  |  | P | P | P
Northdale Blvd | Dale Mabry Hwy | Dawnview Dr | P |  |  |  | P |  | 
 | Dawnview Dr | Claywell Elementary | P | P |  |  | P |  | 
 | Claywell Elementary | Lakeshore Rd | P |  | P |  | P | P | 
Bearss Ave | Dale Mabry Hwy | 22nd St |  | P | P |  | P |  | 
Town N' Country / Egypt Lake |  |  |  |  |  |  |  |  | 
Waters Ave | Sheldon Rd | Anderson Rd |  | P |  | P | P | P | P
 | Anderson Rd | Dale Mabry Hwy |  | P |  |  | P | P | 
 | Dale Mabry Hwy | Florida Ave | P | P |  |  | P | P | P
Sligh Ave/Pinecrest Manor | Benjamin Rd | Dale Mabry Hwy | P |  |  |  | P |  | 
Lambright Rd/Sligh Ave | Dale Mabry Hwy | Armenia Ave | P |  | P |  | P |  | 
Hanley | Hillsborough Ave | Waters Ave |  |  |  |  | P |  | 
Sheldon Rd | Hillsborough Ave | Linebaugh Ave |  |  |  |  | P |  | 

## Slide 18: Corridor Preliminary Recommendations
Facility | From | To | Preliminary Recommendations |  |  |  |  |  | 
 |  |  | Sharrows | Bike Lane | Sidewalks | Midblock Safety (Ped/Rdwy Audit) | Lighting | Roadway/ Intersection Restriping/ Improvement | Transit
Palm River - Coordination with South Coast Greenway |  |  |  |  |  |  |  |  | 
78th St | Madison Ave | Causeway Blvd | P |  |  |  | P | P | 
 | Causeway Blvd | Lee Roy Selmon | P |  |  |  | P |  | 
Maydell Dr | Causeway Blvd | Adamo Dr | P |  |  |  | P |  | 
Citrus Park - Coordination with Upper Tampa Bay Trail |  |  |  |  |  |  |  |  | 
Gunn Hwy | Ehrlich Rd | Citrus Park Dr | P | P |  |  | P |  | 
 | Citrus Park Dr | Henderson Rd |  | P |  |  | P |  | 
 | Tarpon Springs | Van Dyke Rd |  | P |  |  | P |  | 
Brandon Area |  |  |  |  |  |  |  |  | 
Parsons Ave | SR 60 | M L King Blvd |  |  | P |  | P |  | 
Mango Rd (CR579) | M L King Blvd | N of I-4 |  |  | P |  | P |  | 
Providence Rd | Bloomingdale Ave | SR 60 |  |  |  |  | P |  | 
Bloomingdale Ave | US Hwy 301 | Bell Shoals Rd |  |  |  | P | P | P | 
 | Bell Shoals Rd | Cade Ln |  |  |  |  | P |  | 
 | Cade Ln | Lithia Pinecrest |  |  |  |  | P |  | 

## Slide 19: USF Area
  56th Street, 42nd Street and Bruce B. Downs Boulevard ranked in the top 10 study corridors for high bike/ped crashes
  Lack of sidewalks and poor pedestrian visibility along 42nd Street and 46th Street/Skipper Road due to tree canopies
  Need for midblock crossing and sidewalks along 46th Street / Skipper Road at transit stops or student pickup/drop-off locations

## Slide 20: Carrollwood Area
  Fletcher Avenue ranked overall the No. 1 study corridor needing improvements (31/crashes per mile)
  There are no bike lanes along this corridor and very limited room for them
  Midblock crossing(s) along Fletcher Avenue should be considered
  I-275 interchanges at Fletcher and Bearss Avenues need additional pedestrian crossing, signage and pavement markings

## Slide 21: Town N’ Country/Egypt Lake Area
  Veteran’s Expressway crosswalks provide no indicators to vehicles that pedestrians have the right-of-way and should be further evaluated
  High mid-block pedestrian activity at Waters, Hanley and Armenia Avenues
  Need for intersection upgrades to curb ramps, push buttons, and eliminate driveway access to corner businesses.
  Sidewalks needed along Sligh Avenue
    between Benjamin Road and the CSX railroad
    Dale Mabry and Himes

## Slide 22: Citrus Park Area
  Curb radius redesign to reduce speed from Gunn Hwy to Gunn Hwy
  Need for mid-block crossing Gunn Highway between Erhlich Road and Citrus Park Drive
  Need for pedestrian crosswalk with pavement marking is needed at Van Dyke Road signalized intersection
  Potential implementation of rural roadway “sharrows” along Gunn Hwy between Tarpon Road and Van Dyke Road
  Vegetated overgrowth/low lying canopied trees between Erhlich and Henderson Roads

## Slide 23: Palm River and Brandon Areas
  Low speeds and traffic volumes along 78th Street and Maydell Drive may provide opportunity for “sharrows” along both corridors
  Lighting along roadway should be further evaluated
  Continuous sidewalks along most Brandon corridors
  Brandon corridors have the lowest bike/ped crash rates compared to other areas

## Slide 24: Upcoming Steps…
Complete Improvement Recommendations
Prioritize / Rank Improvements by Corridor
Prepare Draft Report