## Slide 1
Florida Avenue and Tampa Street/ Highland Avenue Corridor Study
Project Advisory Group Meeting #3
Identify/Define Alternatives
October 28, 2015

## Slide 2: Study Purpose
Identify and evaluate alternative configurations to determine how to best meet the needs of a wide range of users – current and future.
Florida Ave & Tampa St/Highland Ave Corridor Study

## Slide 3: Study Objectives
Look at how alternatives can:
  Provide safe access between Downtown and Neighborhoods for drivers, transit users, pedestrians, and bicyclists
    Commercial and neighborhood access
  Support the InVision Plan’s vision of the corridor as a neighborhood “main street” and commercial district
  Contribution to the City’s public realm
  Role in the larger transportation network
Florida Ave & Tampa St/Highland Ave Corridor Study

## Slide 4: Project Timeline
Timeline of PAG Meetings:
Florida Ave & Tampa St/Highland Ave Corridor Study
Study Area, Model Assumptions, & Evaluation Criteria
Existing Conditions
Identify Alternatives
Review Alternatives Evaluation
Evaluation Outcomes
#1
#5
#2
#3
#4

## Slide 5: PAG Meeting #3
Meeting Objectives:
  Define the “No Build” alternative
    Include I-275 Express Lanes
  Choose up to four “Build” alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study






## Slide 6: Evaluation Process
Florida Ave & Tampa St/Highland Ave Corridor Study
Multiple Step Evaluation Process:
Reasonability Test
Initial Evaluation
Final Evaluation

## Slide 7: Evaluation Criteria
Florida Ave & Tampa St/Highland Ave Corridor Study
Traffic & Corridor Function
System-Wide Function
Pedestrian & Bicycle Infrastructure
Safety
Transit
Community Impacts
Other
If we do ____, then….

## Slide 8: No Build Alternative
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street
Florida Avenue

## Slide 9: “No Build” Alternative
Florida Ave & Tampa St/Highland Ave Corridor Study
No change to existing lane configuration/ fundamental operating characteristics.
Consider infrastructure enhancements
    Example – sidewalk improvements, additional crossing opportunities, bus stop enhancements, and other minor operational, safety, or aesthetic enhancements.
Used to compare “build” alternatives

## Slide 10: “No Build” Alternative
Florida Ave & Tampa St/Highland Ave Corridor Study
Florida Avenue:
Palm Ave to Floribraska Ave
ROW = 50’

## Slide 11: “No Build” Alternative
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue:
Columbus Dr to MLK Blvd
ROW = 52’

## Slide 12: “Build” Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street
Florida Avenue

## Slide 13: “Build” Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Project scope mentioned the following:
  Two-way throughout study area
  One-way pair with lane reduction and corridor enhancements
  Two-way for portion of study area
  Dynamic lane assignment by time of day

## Slide 14: Alternatives “Family Tree”
Florida Ave & Tampa St/Highland Ave Corridor Study
Existing
Lane Reduction
Two-Way Conversion
Hybrid
Dynamic Lanes

## Slide 15: Two-Way Conversion
Florida Ave & Tampa St/Highland Ave Corridor Study
Two-Way Conversion
Sidewalk & Buffer
8’
Sidewalk & Buffer
8’
Travel
11’
Travel
11’
Cycle Track & Buffer
14’
Florida Ave
Florida Ave
Tampa St
Tampa St

## Slide 16: Two-Way Conversion
Florida Ave & Tampa St/Highland Ave Corridor Study
Traffic Level of Service | Traffic Safety | Community Impact
Slight decline in overall LOS, more noticeable at signalized intersections. Significant decline in peak hour LOS, particularly within the PM peak along Florida Ave. | Potential increase in traffic safety, particularly severity of crashes, as a result of reduced speeds and potential median refuge. | One-way to two-way street conversions have been shown to have positive impacts on community factors, both economically and from an overall livability standpoint.
Pedestrian Environment | Bicycle Environment | Transit
Limited opportunity to enhance the physical pedestrian environment, especially along Florida Ave. As a result of slower traffic, the pedestrian environment may feel more comfortable. However, introducing two-way traffic may introduce new challenges for pedestrians. | Some opportunity to provide enhanced bicycle facilities, particularly along Tampa St, but two-way conversion may require removing the existing bicycle lanes, especially along Florida Ave. | Transit service would most likely shift to one of the roadways, which could lead to some routing efficiencies. Slower traffic could effect bus operations and stopped buses could occasionally impact the flow of traffic.

## Slide 17: Lane Reduction
Florida Ave & Tampa St/Highland Ave Corridor Study
Lane Reduction
Travel
11’
Travel
11’
Sidewalk
10.5’
Sidewalk
10.5’
Buffered Bike
7’
Sidewalk & Buffer
8’
Sidewalk & Buffer
8’
Travel
11’
Travel
11’
Cycle Track & Buffer
14’
Sidewalk
7.5’
Sidewalk
7.5’
Parking
8’
Travel
11’
Travel
11’
Bike Lane
5’
Florida Ave
Florida Ave
Florida Ave
Tampa St

## Slide 18: Lane Reduction
Florida Ave & Tampa St/Highland Ave Corridor Study
Traffic Level of Service | Traffic Safety | Community Impact
May experience slight decline in LOS, particularly within the PM peak along Florida Ave. | Slight increase in overall traffic safety as a result of the reduction in the number of lanes and potentially reduced travel speeds. | Dependent on the designation of the “flex” space. Space could be used to provide on-street parking, landscaping, or enhanced pedestrian/bike/transit environment.
Pedestrian Environment | Bicycle Environment | Transit
Opportunity to enhance pedestrian, bicycle, and/or transit environment exists within the “flex” space. This space could be used to provide for a wider sidewalk, provide buffered/separated bicycle lanes or a cycle track. The space could also be used as an envelope for future transit enhancements along the corridor. |  | 

## Slide 19: Alternatives “Family Tree”
Hybrid
Florida Ave & Tampa St/Highland Ave Corridor Study
Sidewalk
7.5’
Sidewalk
7.5’
Travel
12’
Travel\
Center Turn Lane
11’
Travel
12’
Sidewalk
7.5’
Sidewalk
7.5’
Hybrid
Parking, Travel, Bike
13’
Travel
11’
Travel
11’
Florida Ave
Florida Ave
Tampa St
Florida Ave

## Slide 20: Reversible Traffic Lanes
Florida Ave & Tampa St/Highland Ave Corridor Study
Provide added directional capacity during periods of elevated traffic congestion.
Good signage is critical.
May generate neighborhood concerns (Phoenix).
E Bay St, Jacksonville, FL

## Slide 21: Reversible Traffic Lanes
Florida Ave & Tampa St/Highland Ave Corridor Study
Potential Concerns:
  Perception of less concern about pedestrians and safety of the local residents/businesses – more emphasis on travel speed.
  Left turns can be problematic – may increase cut-through traffic.
  Increase in crashes, particularly head-on and sideswipe crashes (Washington DC & Charlotte)
7th Avenue, Phoenix, AZ

## Slide 22: Time of Day Parking Restrictions
Florida Ave & Tampa St/Highland Ave Corridor Study
Allow for on-street parking during off-peak traffic conditions
Require a good signage and strong enforcement program
N Miami Ave, Miami, FL

## Slide 23: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study

## Slide 24: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
No Build

## Slide 25: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
1. Two-Way Both

## Slide 26: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
2. Lane Reduction Both

## Slide 27: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
3. Two-Way Tampa/Highland, Lane Reduction Florida

## Slide 28: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
4. Two-Way Tampa/Highland, Dynamic Lanes Florida

## Slide 29: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
4A. Two-Way Tampa/Highland, Reversible Lanes Florida
AM
Mid-Day
&
Night
PM
-OR-

## Slide 30: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
4B. Two-Way Tampa/Highland, Parking Lane Florida
AM
Mid-Day
&
Night
PM
P
P

## Slide 31: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
5. Dynamic Lanes Both

## Slide 32: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
5. Dynamic Lanes Both
AM
Mid-Day
&
Night
PM
-OR-

## Slide 33: Define the Alternatives
Florida Ave & Tampa St/Highland Ave Corridor Study
Tampa Street/Highland Avenue
Florida Avenue
5. Dynamic Lanes Both
AM
Mid-Day
&
Night
PM
P
P

## Slide 34: Build Alternatives Selection
Florida Ave & Tampa St/Highland Ave Corridor Study

## Slide 35: Model Data Needs
Florida Ave & Tampa St/Highland Ave Corridor Study
Necessary data to evaluate the alternatives

## Slide 36: Next Steps
Evaluate Alternatives
Summarize and Document Final Evaluation
Florida Ave & Tampa St/Highland Ave Corridor Study

## Slide 37: Next PAG Meeting
Florida Ave & Tampa St/Highland Ave Corridor Study
Study Area, Model Assumptions, & Evaluation Criteria
Existing Conditions
Identify Alternatives
Review Alternatives Evaluation
Evaluation Outcomes
#1
#5
#2
#3
#4

## Slide 38: Review Evaluation of Alternatives
Evaluate each alternative for its impacts to multimodal mobility and traffic safety/operations
  Preliminary outcomes of the evaluation criteria/measures of effectiveness for each alternative
  Adjust MOEs/weighting criteria, as appropriate
Florida Ave & Tampa St/Highland Ave Corridor Study

## Slide 39
Florida Avenue and Tampa Street/Highland Avenue Corridor Study